## Slide 1
Unsupervised learning for
Indoor Localization and Floor Mapping
Max Maguire

## Slide 2: Motivation
GPS inaccessible settings
  Line-Of-Sight
Power efficiency
Higher precision localization
  Beam forming
  VR/AR
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram

## Slide 3: Context
* Zahid Farid, Rosdiadee Nordin, and Mahamod Ismail
“Recent Advances in Wireless Indoor Localization Techniques and Systems” 2013
Pedestrian Dead Reckoning
Transforms raw Data into state estimates using process model
  Position
  Orientation
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram

## Slide 4: Experimental Set-Up
Raw Data:
- 3-axis Accelerometer, Gyroscope, Magnetometer
- 100 hz
Step Calibration:
- 9 recordings of set length/step count
Number of recordings:
- 17 trials
- 5 different paths
* https://www.cmu.edu/finance/property-space/floorplan-room/acad-admin/BPH/index.html
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram
Notes: Alpha shape

## Slide 5: Data Flow Diagram
EKF
Raw Data
Trajectory Model
Step Detection
Segmentation
Classification
Floor Mapping
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram

## Slide 6: Extended Kalman Filter
EKF
Raw Data
Trajectory Model
Step Detection
Segmentation
Classification
Floor Mapping
Incorporates uncertainties into the process and observation models.
Corrects for potential sources inaccuracies using Bayesian inference and joint probability distributions.
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram
Notes: Implement EKF in order to estimate orientation of phone. The Extended Kalman filter is a version of the Kalman filter that works for non-linear problems. Instead of using a fixed matrix for the state and observations equations, we are computing the Jacobian matrix to linearize about an estimate of the current mean and covariance.
Inputs: accelerometer, gyroscope and magnetometer.
Sources of error: Drift, Noise, Bias
In addition to the in-line bias estimation of some of the sensors, we take into account the potential local disturbances of the magnetic field and the effects o f body motion
The relation between body coordinate vectors and global coordinate vectors are non-linear.

## Slide 7: Extended Kalman Filter
EKF
Raw Data
Trajectory Model
Step Detection
Segmentation
Classification
Floor Mapping
Initialize Filter Design
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram
Notes: State Transformation model
Find the Dynamic System of the State
Discretize it via Taylors Expansion
- The measurement vector in our case is a discrete sampled signal from the devices. Therefore, we need to transform our model to a discrete time model.
Observation Transformation model
Find the Dynamic System of the State
Discretize it via Taylors Expansion
- The measurement vector in our case is a discrete sampled signal from the devices. Therefore, we need to transform our model to a discrete time model.
Rrot is the rotation matrix from the body coordinate to the global coordinate,

## Slide 8: Extended Kalman Filter
EKF
Raw Data
Trajectory Model
Step Detection
Segmentation
Classification
Floor Mapping
Update
Predict
z
x
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram
Notes: PREDICT:
Predict next state
Project process uncertainty into state space
Map state estimate back into measurement space
UPDATE:
Find residual between observation and prediction
Calculate covariance of residual
Compute Kalman gain (weighted priority to prediction vs observation based on uncertainties)
Update state estimate using [Kalman gain]
Update state covariance using [Kalman gain]

## Slide 9: Step Detection
EKF
Raw Data
Trajectory Model
Step Detection
Segmentation
Classification
Floor Mapping
Used to infer distance traveled
- Additional measure against cascading error from noisy measurements
Steps
Take Euclidean norm of 3-axis accelerometer data
Filter out high frequency noise
Apply Step Detection Threshold
Track range of signal peaks and valleys
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram
Notes: Method:
Used to infer distance traveled rather than integrating Accelerometer data.
- Designed to account for sudden orientation and attitude shifts of the phone during a walk.
- Additional measure against superposing error from noisy accelerometer data recordings
Take Euclidean norm of 3-axis accelerometer data
Smooth/filter out high frequency noise
Apply Step Detection Threshold
Record Valley and peaks
Solve for Step length coefficient
Smoothing: Moving average of 5 frames operated as a low pass filter (reducing strength of signals > 5hz)
Step Detection threshold: Established during calibration as 3*sigma

## Slide 10: Step Detection
EKF
Raw Data
Trajectory Model
Step Detection
Segmentation
Classification
Floor Mapping
2. Smoothing:
1. Accelerometer Magnitude:
5 frame Convolution window
Steps
Convolution window (Uniform Dist.)
Convolution window (Normal Dist.)
Results of Convolution based Smoothing
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram
Notes: Method:
Used to infer distance traveled rather than integrating Accelerometer data.
- Designed to account for sudden orientation and attitude shifts of the phone during a walk.
- Additional measure against superposing error from noisy accelerometer data recordings
Take Euclidean norm of 3-axis accelerometer data
Smooth/filter out high frequency noise
Apply Step Detection Threshold
Record Valley and peaks
Solve for Step length coefficient
Smoothing: Moving average of 5 frames operated as a low pass filter (reducing strength of signals > 5hz)
Step Detection threshold: Established during calibration as 3*sigma

## Slide 11: Step Detection
EKF
Raw Data
Trajectory Model
Step Detection
Segmentation
Classification
Floor Mapping
4. Step Magnitude:
3. Filtering:
Step Detection threshold, Blanking window
Steps
Step Detection Filter
Step Magnitude α Calibration
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram
Notes: Erroneous steps that were detected due to high frequency noise occurring at the threshold were discarded using a 0.3s blanking window following the onset of each step detected.
Smoothing: Moving average of 5 frames operated as a low pass filter (reducing strength of signals > 5hz)
Step Detection threshold: Established during calibration as 3*sigma

## Slide 12: Trajectory Model
EKF
Raw Data
Trajectory Model
Step Detection
Segmentation
Classification
Floor Mapping
Step Detection
Quaternion to Euler Angles
Trajectory
γ
X
Y
Z
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram
Notes: Segment threshold (45 degrees)
Feature space:
length of the segment,
average time spent per step,
coordinates of the center of the segment

## Slide 13: Segmentation
EKF
Raw Data
Trajectory Model
Step Detection
Segmentation
Classification
Floor Mapping
Example
Trial 3: Corridor turn
Raw Trajectories
Heading Displacement
Segmented
Trajectories
Room
Corridor
Segment
Lengths
Decision Tree
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram
Notes: Segment threshold (45 degrees)
Feature space:
length of the segment,
average time spent per step,
coordinates of the center of the segment

## Slide 14: Classification
EKF
Raw Data
Trajectory Model
Step Detection
Segmentation
Classification
Floor Mapping
- Find “k” neighbors of every point, and identify core points
- Find connected components of core points
- Assign non-core points to nearby clusters at at most distance ε, otherwise assign them to noise
Pros
Unsupervised
Robust to noise
Cons
Sensitive to Tuning
DBSCAN
(Density-Based spatial clustering algorithm with noise)
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram
Notes: Feature space is composed of parameters:
Length
Center
Time spent
Clustering methods: DBSCAN vs Kmeans/KNN
Core point: = minPoints, epsilon

## Slide 15: Classification
EKF
Raw Data
Trajectory Model
Step Detection
Segmentation
Classification
Floor Mapping
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram
Notes: Feature space is composed of parameters:
Length
Center
Time spent
Clustering methods: DBSCAN vs Kmeans/KNN
Core point: = minPoints, epsilon

## Slide 16: Floor Mapping
EKF
Raw Data
Trajectory Model
Step Detection
Segmentation
Classification
Floor Mapping
Draw a 2D alpha shape of the trajectory segments with alpha radius A.
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram
Notes: Alpha shape

## Slide 17: Discussion
Moving Forward…
Finding Anchor points
  Anomalies from environment
  Expanding Feature space
    Gait Analysis
    Additional Sensors
Scale application for larger database
Discussion
Introduction
Algorithms
Experimental Set-Up
Data Flow Diagram
Notes: Alpha shape